## Slide 1: ANC 2019 Conference, Manchester
Emma Greenland PhD BEng MIOA
Anderson Acoustics
Children with hearing loss in mainstream classrooms and implications for acoustic design

## Slide 2
Aim :
To establish reasonably adjusted acoustic criteria (robust, practicable) to ensure that the acoustic design does not place people with disabilities at a disadvantage.
Reason: To improve access to the mainstream classroom by disabled children.

## Slide 3: Requirements and Drivers
Building Regulations
Approved Document E, BB93
Approved Document M, BS 8300: 2018
EFSA Output Specification
The Equality Act
Public Sector Equality Duty

## Slide 4
The Public Sector Equality Duty
Public bodies in England (and non-devolved bodies in
Scotland and Wales)

## Slide 5
Who the general duty applies to
Public authorities listed in Schedule 19 of the Equality Act (e.g. local authorities, FE and HE bodies, schools, health bodies, police, fire and transport authorities, government departments).
Public, private, or voluntary organisations carrying out public functions (including on behalf of a public authority). The Equality Act uses the same definition as the Human Rights Act 1998 (which was used for the gender and disability equality duties).

## Slide 6
In order to fulfil their duties under the Equality Act 2010, school client bodies should anticipate the needs of deaf and other disabled children as current and potential future users of the school.
(Building Bulletin 93)

## Slide 7
Permanent hearing impairment
AD/HD, Autistic spectrum disorder
Speech, language & communication needs
Auditory processing disorder
Mild or temporary hearing impairment
Visual impairment
‘Special hearing & communication needs’, SHCN
‘Deaf and other Disabled Students’ – The BB93 Definition

## Slide 8: The Public Sector Duty
…says that protected groups must not be placed at a disadvantage.
It requires all schools to prepare and implement an accessibility strategy to improve the physical environment of the school for pupils with SEND, including those with Special Hearing and Communication Needs:
by making reasonable adjustments to put children with SEND on a more level footing.
The Equality Act also covers age discrimination:
and people with English as an Additional Language (EAL):
Both may be disadvantaged by poor acoustic conditions and so the needs of these protected groups must also be considered.

## Slide 9: Requirements (BB93)
SEN rooms, designated units or specialist resource provision
Practicable for smaller rooms (low occupancy, high staff:student ratio)
Based on assumed vocal effort and communication distance for SNR
15 dB SNR recommended by ASHA, 20 dB SNR recommended by BATOD
Shorter RT for younger children

## Slide 10: Requirements
School Premises Regulations
“where pupils with special needs are taught in mainstream schools, the acoustics of the spaces where they are taught may need to be enhanced to the same standards as those special units”,
“provision will usually be required to teach these pupils in smaller groups so that noise from other pupils is lower and the distance between teacher and pupil is minimised”.
IOA/ANC Design Guide
Pupils with SHCN should be taught in rooms which meet BB93 acoustic criteria for SHCN rooms.
‘specialised provision may be directly attached to a mainstream class in the form of a ‘quiet room’ leading from the classroom’.

## Slide 11: Requirements
The Equality Act 2010 requires schools to make ‘reasonable adjustments’ to put children with disabilities on a more level footing.
Sending children to an SHCN enhanced quiet room to access the majority of their teaching and learning… inclusive practice?
ESFA Output Specification
‘People with disabilities, including those with a hearing impairment, must not be placed at a disadvantage by the design of the Building’.
Ensure and demonstrate that all layouts allow for disabled pupils to be able to access all activities on offer in at least one space of each type or within each suite.

## Slide 12
UN Convention on The Rights
of Persons with Disabilities
Guarantees all disabled pupils and students a right to participate in all forms of mainstream education with appropriate support.
UK has replaced restrictions on its obligations:
Definition of ‘general education system’ changed to ‘segregated education’ (Mainstream + Special Schools)
Reserves the UK’s right to send disabled children to special schools outside their local area.
It is the only country in the world apart from Mauritius to do so.
Article 24: A right to Inclusive Education

## Slide 13
Prevalence of SHCN
Analysis of 2018 figures for state funded
primary and secondary schools

## Slide 14
4.7m children
16,766 schools
Prevalence – mainstream state schools
3.2m children
3,436 schools
7.9m children in 20,202 schools
EAL
19%
1.5m children
SHCN
AD/HD, Autistic spectrum disorder
Speech, language & communication needs
Auditory processing disorder
Mild or temporary hearing impairment
Visual impairment
Permanent hearing impairment
6%
240,000 children
Young children
4.7m children

## Slide 15
Prevalence – by individual need
23,000 HI children
up to 1 per primary school
up to 2 per secondary school

## Slide 16
Young children (Primary schools)
English as additional language EAL
Special hearing & communication needs SHCN
Prevalence – by typical classroom size
National averages should be treated with caution
Prevalence varies with individual school location and circumstances…
but the need to provide appropriate conditions for children with SHCN should be anticipated in every classroom
Where there is significantly higher prevalence in a school cohort, consider specialist resource provision or designated unit
2 SHCN per classroom
1 SHCN per classroom

## Slide 17
Prevalence – what the teachers say
Anderson Acoustics teacher survey 2016

## Slide 18
Attainment – by individual need
Attainment English + Maths progress scores
Attainment gap for HI is significant (remember it’s not a learning disability), but it is smaller than for other forms of SHCN.
-10%
-30%
-25%
EAL
Lower at start of school, eliminated by age 16

## Slide 19
Quality of research
Attainment
-10%
-30%
-25%
Speech perception research quality
high
low
N/A
N/A
low

## Slide 20
The challenge
how to improve accessibility

## Slide 21: Constraints
Not feasible to apply BB93 enhanced standard to mainstream classrooms:
Providing sound absorption to achieve <0.4s Tmf vies with spare wall space, and trends for exposed soffits for sustainability
DfE budget does not allow for provision of extra bass sound absorption to achieve <0.6s T125Hz
<0.4s Tmf not appropriate as early sound reflections needed to support teacher’s voice and avoid vocal strain.
Not feasible to target 30 dBA noise (number of children in the space, priority for natural ventilation, practicable limit that even the quietest natural ventilation systems can achieve).
The standard school building budget does not allow for provision of enhanced partition and door constructions to achieve enhanced sound insulation criteria.
Current funding crisis => diminishing resources to teach SHCN in small groups

## Slide 22: Reasonable adjustments - holistic approach
Company LOGO
classroom management
listening aid
acoustic design

## Slide 23: Classroom management
‘effective classroom management by the teacher is critical in ensuring that the pupils can have access to all that is spoken’. (IoA/ANC Design Guide)
Primary responsibility of acoustic design is teacher-to-student comms in quiet.
classroom management

## Slide 24: Personal listening aids
listening aid
Given the low prevalence of SHCN, and the very low prevalence of children with hearing impairment, personal listening aids are feasible strategies to help boost acoustic conditions and support access to learning.
“personal listening aids enhance SNR, reduce impact of unhelpful reverberation, particularly when a headset is used by the speaker”
“if ambient noise level [SNR] is controlled then high RT has a minimal effect when a personal listening aid is in skilled use and set up properly”
British Association for Teachers of the Deaf (BATOD)
Image courtesy of Phonak
IoA/ANC Design Guide

## Slide 25: Factors Affecting Speech Perception
SNR is most important factor
RT also has an impact
0.2-0.5 s RT is ideal
but up to 0.9 s RT acceptable
(normal hearing children)
Non-zero RT to support voice:
≥ 0.5 s RT ideal
Low frequency RT control cited important for hearing impaired
… evidence?
…evidence when personal listening aid used?
acoustic design

## Slide 26
The study
Quantifying the listening gap

## Slide 27
Quantifying the listening gap
Seminal research studies reviewed, based on subjective speech perception testing, in varied acoustic conditions up to 1.0 s RT (flat-ish spectrum)
Listening gap: difference in % perception scores between ‘impaired’ and non-impaired groups
Reveals inherent % listening gap (ideal acoustic conditions)
acoustic % listening gap (non-ideal conditions)
consistencies between studies (systematic errors/variations reduced)
Note:
No studies analysed or controlled for age.
All studies used multitalker babble as noise source
Benefit of personal listening aids not investigated
Uplift in low frequency RT not investigated

## Slide 28: Results
Mild to moderate hearing Loss
Severe to profound hearing Loss
English as additional language
AGE
Minimal

## Slide 29: Results – inherent listening gap
Company LOGO
For some needs, even in optimum acoustic conditions (silent, anechoic), children still experience reduction in speech perception scores compared to their typical peers:
Children with hearing loss are most disadvantaged.
Even when secondary school classrooms are BB93 compliant, listening disadvantage could be up to 40% (reducing to 20-30% with a personal listening aid).
For milder needs, inherent listening gap is small, 4% or less, not significant as comparable to variation within the impaired group.
However these needs are still significantly affected by poor acoustics. For example, in BB93 compliant primary school refurbs, the listening gaps could double.

## Slide 30: Results – ideal acoustic conditions
Company LOGO
To eradicate additional listening gap caused by acoustics:

## Slide 31: Boost from personal listening system
Company LOGO
In BB93 compliant classrooms, even at good SNR of ≥15 dB, the listening gap for S-P hearing loss will be 30-40%
…but a personal listening device
> removes effect of reverberation
> boosts SNR.

## Slide 32: Recommendation – reasonable adjustments

## Slide 33: Next steps for reasonably adjusted criteria for inclusion
DfE are looking at this issue for latest OS – November 2019
ANC/IoA Consultation on reasonably adjusted criteria
Cost of achieving 0.5 s Tmf against other design constraints
Evidence for reverberation time of 0.6 s at 125 Hz?
Use of personal listening systems
  Procurement
Views of other professionals:
  BATOD
  Educational audiologists
  Speech and language therapists

## Slide 34
Feedback please!
emma@andersonacoustics.co.uk