## Slide 1: WHO Environmental Noise Guidelines for the European Region Charlotte Clark Associate, Acoustics
Annual Conference 6th June 2019 Manchester

## Slide 2: Scope of presentation
Aim of the Guidelines
Methodology used to set the Guidelines
Evidence reviews
What the guidelines say
A few personal thoughts on the guidelines and the evidence review process

## Slide 3: Aim of the Guidelines
To provide recommendations for protecting human health from exposure to environmental noise*
  Road
  Rail
  Aircraft
  Wind turbine
  Leisure noise
Guidelines focus on the WHO European Region but seen to have global relevance/application
* Outdoor noise for all sources, except leisure noise which is indoor and outdoor

## Slide 4: Scope of the Guidelines
In the general population exposed to environmental noise, what is the exposure-response relationship between environmental noise (reported as various indicators) and the proportion of people with a validated measure of health outcome, when adjusted for confounders?
In the general population exposed to environmental noise, are interventions effective in reducing exposure to and/or health outcomes from environmental noise?

## Slide 5: Scope of the Guidelines
Guidelines are source specific not environment specific
They do NOT include
  occupational and industrial noise
  neighbourhood noise
  combined exposures
  hospital noise
The Community Noise Guidelines (1999) still stand for anything not covered in the new Guidelines

## Slide 6: Guideline Development
Systematically review scientific evidence
  Health effects of environmental noise
  Effectiveness of interventions to reduce exposure and improve health
Provide evidence-based recommendations
  Exposure - response relationships
  Effectiveness of interventions

## Slide 7
Health outcomes reviewed
  Cardiovascular diseases (including diabetes and metabolic effects)
  Annoyance
  Sleep disturbance
  Cognitive impairment
  Hearing impairment and tinnitus
  Adverse birth outcomes
  Quality of life, mental health and wellbeing
  Interventions to reduce noise and improve health
All the systematic reviews are free to download in a special issue of the International Journal of Environmental Research and Public Health
https://www.mdpi.com/journal/ijerph/special_issues/WHO_reviews

## Slide 8
Health outcomes reviewed
 | Pages – Main paper | Pages – Supplementary material
Cardiovascular diseases inc metabolic | 59 | 0*
Sleep disturbance | 45 | 31
Annoyance | 39 | 73
Cognitive impairment | 23 | 64
Hearing impairment and tinnitus | 19 | 16
Birth outcomes | 16 | 8
Quality of life, wellbeing, mental health | 27 | 40
Interventions | 44 | 27
Page Totals | 272 | 259
Over 500 pages
and that excludes * the RIVM detailed report of 260 pages on cardiovascular diseases

## Slide 9
GRADE evidence
For each body of evidence and noise source one evidence rating is provided.
High quality: further research very unlikely to change certainty of effect estimate
Moderate quality: further research is likely to have an important impact on the certainty of the effect estimate and may change the estimate
Low quality: further research is very likely to have an important impact on the certainty of the effect estimate and is likely to change the estimate
Very low quality: any effect estimate is uncertain
Low quality does not necessarily mean that exposure to noise has no effect on the health outcome, but encourages further research to improve the quality of the evidence.

## Slide 10
Guidelines relate to a specific increase in risk for a health outcome
Priority health outcomes (DW)
Relevant risk increase for setting guideline level
Most of the guidelines are actually set in relation to a 10% increase in annoyance and 3% increase in sleep disturbance.
Important to appreciate that the new Guidelines are not LOAEL or SOAEL values or limits or caps - they do not indicate where noise effects begin for these health outcomes.
They are noise exposure levels above which the WHO is confident there is an increased risk of adverse health effects
Notes: Definition: Noise exposure levels above which the WHO is confident there is an increased risk of adverse health effects
Assessment of validity of exposure-response functions (ERF) from systematic reviews
Assessment of lowest noise level measured in the studies reviewed
Assessment of the smallest relevant risk increase for each adverse health outcome
Determination of guideline exposure level based on ERF, starting from lowest level measured and associated with smallest relevant risk increase for adverse health outcomes
Selection of guideline level for each noise source based on priority health outcome with lowest exposure level for that source
Benchmark values, not effect thresholds

## Slide 11
Strength of guideline recommendations
Priority health outcomes (DW)
Relevant risk increase for setting guideline level
A strong recommendation can be adopted as policy in most situations. The guideline is based on the confidence that the desirable effects of adherence to the recommendation outweigh the undesirable consequences. The quality of evidence for a net benefit combined with the other factors – inform this recommendation, which should be implemented in most circumstances
A conditional recommendation requires a policy-making process with substantial debate and involvement of various stakeholders. There is less certainty of efficacy due to lower quality evidence, opposing values and preferences, high resource implications… meaning there may be circumstances or settings in which it will not apply

## Slide 12: Where do the new Guidelines sit in relation to other WHO Guidelines?
“The current environmental noise guidelines for the European Region supersede the Community Noise Guidelines from 1999. Nevertheless, the GDG recommends that all CNG indoor guideline values and any values not covered by the current guidelines (such as industrial noise and shopping areas) remain valid.”
The current environmental guidelines for the European region complement the Night Noise Guidelines 2009.
GDG= Guideline Development Group

## Slide 13: Don’t shoot the messenger….

## Slide 14: Headlines
New exposure-response functions for air, road traffic and railway noise for annoyance; cardiovascular outcomes; and sleep disturbance.
Narrative reviews of cognitive impairment; quality of life, wellbeing and mental health; hearing impairment and tinnitus; birth outcomes; and interventions.
Across the board highlights the need for further methodologically robust studies and standardized methodologies, where possible.
Review of interventions - highlights what evidence is available and need for further studies of this nature.
There are still very few papers on combined exposures, yet many people do not live in a one source situation.
This Photo by Unknown Author is licensed under CC BY-SA-NC

## Slide 15: Recommendations for aircraft noise

## Slide 16: Annoyance – aircraft WHO 2017
Figure from Guski et al, 2017, IJERPH
WHO 10% HA ~45dB Lden

## Slide 17: Recommendations for road traffic noise

## Slide 18: Recommendations for railway noise

## Slide 19: Recommendations for wind turbine noise

## Slide 20: Recommendations for leisure noise

## Slide 21: Interventions
Covers publications 1980- 2014
Considers interventions for air, road traffic and railway noise across the range of health outcomes
Many of the interventions were associated with changes in health irrespective of the source type, the outcome or intervention type
Highlights the excess-change response for annoyance
Highlights need for further intervention studies – we have now been saying this for years!!

## Slide 22: Annoyance
Notes: Covers publications 2000- 2014
New meta-analyses and exposure-response functions for air, road, railway, and wind-turbine noise
GRADE quality of evidence of exposure‐response relations between noise levels and %HA is moderate (aircraft and railway) or low (road traffic and wind turbines).
The exposure-response relations for road and railway are similar to past reviews (EU, 2002) but markedly higher for aircraft noise.

## Slide 23: Annoyance – aircraft WHO 2017
Figure from Guski et al, 2017, IJERPH
Comparing the studies, a huge range of % highly annoyed is found for the same Lden dB exposure……
%HA is ~10% for study at Ho Chi Minh airport
%HA is ~68% for study Athens airport
……..should we be drawing a line through these data points?

## Slide 24: Annoyance – aircraft WHO 2017
Figure from Guski et al, 2017, IJERPH
SoNA 10% HA ~54dB LAeq 16h
WHO 10% HA ~45dB Lden

## Slide 25: Annoyance – aircraft Gjestland 2018
Figure from Gjestland et al, 2018, IJERPH
10% HA
For this alternative set of data 10% HA corresponds to exposure to aircraft noise at DNL 53.4 dB - substantially higher than the WHO guideline value Lden 45 dB.
However, this paper is NOT a systematic review
10% HA

## Slide 26: Annoyance
It is a concern that the strength of the relationship between aircraft noise and annoyance varies greatly depending on which studies are included in the meta-analysis.
The WHO Guidelines suggests that the wide variation between studies because of situational and contextual differences.
The Guidelines state, that for health assessments instead of using the generalised WHO 2017 annoyance ERFs
“…data and exposure-response curves derived in a local context should be applied, whenever possible to assess the specific relationship between noise and annoyance in a given particular situation. If, however, local data is not accessible, the general exposure-response relationships can be applied, assuming that the local annoyance follows the generalized average annoyance.” (Section 5.4)

## Slide 27: Cardiovascular disease
Basner et al., (2014) estimated that risk for cardiovascular outcomes such as high blood pressure, AMI, and stroke, increases by 7 to 17% for a 10dB increase in aircraft or road traffic noise exposure.
Vinneau et al., (2015) found that risk for incident ischaemic heart disease increased by 4% (95%CI 1.00-1.10) per 10dB Lden increase in road traffic noise exposure.
Figure from van Kempen et al, Cardiovascular and metabolic effects of environmental noise, RIVM Report 2017
WHO - Relative Risk of 1.08 (95% CI: 1.01–1.15) per 10 dB (Lden) for the association between road traffic noise and the incidence of Ischaemic Heart Disease.
Notes: Covers publications January 2000-August 2015
New meta-analyses for a range of cardiovascular outcomes
Lots of studies show an association but many are not methodologically robust
GRADE – studies often low quality
Concludes that the results of this updated review are similar to those of past reviews

## Slide 28: Self-reported sleep disturbance
Noise was associated with self-reports of being highly sleep disturbed when the question referred to noise, but not when the question did not refer to noise.
Figure – ERF for self-reports of noise and high sleep disturbance where the questions referred to noise (black= WHO 2018, red=Miedema EU curve)
Figures Basner and McGuire, 2018, IJERPH

## Slide 29: Awakenings - sleep disturbance
Figures Basner and McGuire, 2018, IJERPH
Figure – Exposure Response Function for probability of additional awakening
The odds ratio for the probability of awakening for a 10 dBA increase in the indoor Lmax was significant for:
aircraft (1.35; 95% CI 1.22–1.50)
road (1.36; 95% CI 1.19–1.55)
rail (1.35; 95% CI 1.21–1.52)
Urgent need for more studies of awakenings given the community importance of this issue.

## Slide 30: Some personal observations
The setting of the guidelines are driven by the ‘classic’ health outcomes of annoyance and sleep disturbance
The metrics used in the guidelines are not those we need for noise and health assessment to consider the daytime period (leads to converting metrics – see Brink et al, International Journal of Hygiene and Environmental Health 2018)
Lden conflates health effects into the metric
There are benefits of setting guidelines by noise source but this is at the cost of guidelines for specific settings (e.g. is it useful to use Lden for schools?)

## Slide 31: Some personal observations
No economic cost-benefit assessment of setting the guidelines at these levels has informed the guidelines. Should we set guidelines for noise and health that ignore the economic and social value of transportation?
Are there enough people involved in the setting of the Guidelines who
  1) make noise
  2) try and mitigate noise?

## Slide 32
Thank you
Any questions?
Charlotte.Clark@arup.com